## Slide 1
SL1680 Edge-AI Terminal · Project Overview
2026-07-28 · v2.7 · Synaptics SL1680 (Astra Dolphin RDK)
Local Voice AI
DL7400 4-Display
TD7800 Touch Panel
Recovery 9/9
Open-source Astra SDK + borrowed RDK/EVK + self-purchased peripherals | fully measured

## Slide 2
1 · What This Is
2/11
An edge-AI human-machine terminal:
local voice AI (ASR/TTS fully on-board) + dual display chains (DL7400 USB multi-display + TC358775 direct-drive LVDS touch panel) + visual wake-up
Only the dialogue brain is cloud (DeepSeek); local fallback model offline; everything survives power loss
Test conditions
Open SDK
GitHub Astra SDK (Yocto scarthgap)
Borrowed
SL1680 RDK ×1 + DL7400 EVK ×1
Purchased
C920 / 4 monitors / TM10.5 panel / LAMTL / audio kit

## Slide 3
2 · System Architecture
3/11
[C920 camera] ─USB→ NPU: person detect 25ms/frame → visual wake greeting
[C920 mic] ─USB→ CPU: silero VAD → SenseVoice ASR(int8) → 4-layer routing
① local volume ② local device ③ web search + grounding ④ cloud DeepSeek
→ matcha TTS → ALSA astraout → [HT517 amp + speaker] (I2S)
Display A: dl_face → GStreamer → [DL7400] ─USB3→ up to 4 monitors
screen0 = face + bilingual subtitles screen1 = live camera
Display B: weston → DSI 4-lane → [LAMTL / TC358775] ─LVDS→
[TM10.5-TD7800 1280×720 touch panel] (touch I2C+INT back, ~120Hz)
Cloud: DeepSeek + Zhipu standalone search Offline fallback: local qwen2.5-0.5b

## Slide 4
3 · Three Achievement Domains
4/11
A · Local Voice Terminal
RTF 0.197
Fully local ASR+TTS; 4-layer routing; visual wake; mic guard 0 idle-spin
B · DL7400 Multi-Display
4 screens
8.7/5.8/15.0/5.7 fps concurrent; bottleneck = DL streaming; 3 SDK defects reported
C · TD7800 Touch Panel
6 root causes
DSI→LVDS direct drive lit; touch 120Hz; SPI debug channel; recovery 9/9
One engineering discipline across all three: the board is the truth · immediate backflow · sha256 reconciliation · byte-level acceptance

## Slide 5
3A · Local Voice-AI Terminal
5/11
Models: mobilenet (NPU) · silero VAD · SenseVoice int8 · matcha+vocos · qwen2.5-0.5b fallback · cloud deepseek-chat

## Slide 6
3B · DL7400 USB Multi-Display
6/11
4
screens at once
2×4K + 2 hi-res
8.7/5.8/15.0/5.7
concurrent fps
USB3 total constant
−20%
4K when 3→4
7.2 → 5.8 fps
×3
SDK defects filed
with DisplayLink
• Pipeline measured stage-by-stage: 111 → 31.9 (HW scale) → 7.4 fps — bottleneck is DL streaming
• Three SDK defects: hotplug callback always fails / EDID & modes all cached / dpaux on a dead sink blacks out everything
• No self-heal after monitor power loss — workaround: voice "re-detect screens"

## Slide 7
3C · TD7800 Direct Drive: Six Root Causes
7/11
Key formula: LVDS pclk = DSI clock-lane freq ÷ PCLKDIV; DSI must keep margin (vendor 4.4%, ours 33%)
Companions: SPI tool (ID / BIST / NVM read) · 120 Hz multitouch · 180° rotation + calibration · recovery 9/9

## Slide 8
4 · Key Knowledge Distilled
8/11
1 DSI→LVDS bridges need bandwidth margin (zero = live noise)
2 TDDI resets always tied high in hardware
3 3.3V into 1.8V pins back-feeds via ESD (measured 2.38V)
4 Never trust EDID preferred_mode (the 160 Hz trap)
5 Non-48 kHz rates crash the audio driver (astraout is required)
6 Zhipu chat web_search is fake (standalone API + grounding)
7 Yocto: FetchContent hard-off / .so packaging / :pn- scope / debugfs-level acceptance
8 The board is the truth: backflow + sha256
9 Remote ops: script files / busybox gaps / BOM guard

## Slide 9
5 · Assets & Current State
9/11
Software / hardware assets
Board state (measured)
Document navigator: §9 of this overview indexes all 20+ topic documents (CN/EN), from top level down to source code

## Slide 10
6 · Known Open Issues (honest list)
10/11
Why KWS is #1:
Kills false triggering (saves API cost) and unlocks the pause/wake interaction loop — assets and binaries already on board

## Slide 11
7 · Roadmap
① Integrate KWS
Fixes false triggering + unlocks pause-by-voice; assets ready, ~0.5–1 day
② Deliverable image
Real-hardware flash verification + rootfs trio into Yocto — colleagues get everything in one flash
③ Robotics
SL1680 torso + TM10.5 face + DL7400 teleop console + finger actuators — aligned with Synaptics' interfaces-for-robotics narrative
SL1680 Project Overview v2.7 · 2026-07-28 · full doc set (MD/HTML/PDF/PPTX × CN/EN) in the project folder